Cross-Town Rail Link Schematic

Positions of fixed-distant boards, level-crossing speed-restriction and advance-warning boards to be determined.

# PJM 14/02/2007

## Down Train departing Harbour Station

- Train-crew use the token key-switch to start the Britannia Bridge crossing warnings

- Starting signal clears after the warnings have been operating for time

- Train departs, passing over the Britannia Bridge crossing

- Train passes the treadle at Gas Works Siding 
Provided this is within 90 seconds of passing over the Britannia Bridge crossing:
	a) Snowdon Street crossing warnings start
	b) annunciator sounds at Cambrian Crossing: crossing keeper sets crossing for WHR train

- Train passes over the Snowdon Street automatic crossing

- Train passes over the Cambrian Crossing

- Crossing keeper resets the Cambrian Crossing for NR trains

## Loco departing Harbour Station for Gas Works Siding

- Loco-crew use the token key-switch to initiate the Britannia Bridge crossing warnings

- Starting signal clears after the warnings have been operating for time

- Loco departs, passing over the Britannia Bridge crossing

- Loco stops before the siding points, while the crew unlock the ground-frame

- Loco shunted to siding

- Loco-crew relock the ground-frame, and return the token to its designated place at Harbour station.

## Loco departing Gas Works Siding for Pont Croesor

- Loco-crew obtain the token, and unlock the ground-frame

- Loco shunted out of siding

- Loco-crew relock the ground-frame, and telephone Cambrian Crossing keeper to warn of their approach

- Loco passes over treadle, which is ineffective because Britannia Bridge crossing not previously operated

- Loco proceeds to the Snowdon Street crossing signal

- Loco-crew use the token key-switch to start the crossing warnings

- Train passes over the Snowdon Street crossing

- Train passes over the Cambrian Crossing

- Crossing keeper resets the Cambrian Crossing for NR trains

## Down Works Train departing Harbour Station (out of hours)

- Train-crew use the token key-switch to initiate the Britannia Bridge crossing warnings

- Starting signal clears after the warnings have been operating for time

- Train departs, passing over the Britannia Bridge crossing

- Train passes the treadle at the Gas Works Siding 
Provided this is within 90 seconds of passing over the Britannia Bridge crossing:
	a) Snowdon Street crossing warnings start
	b) annunciator disabled at Cambrian Crossing when unmanned

- Train passes over the Snowdon Street automatic crossing

- Train stops before the Cambrian Crossing, for the train-crew to operate the crossing

- Train passes over the Cambrian Crossing

- Train stops after the Cambrian Crossing, for the train-crew to reset the crossing for NR trains

- Train departs for Pont Croesor

## Up Train arriving Harbour Station from Pont Croesor

- Train passes over the train-approaching treadle, sounding the annunciator at the Cambrian Crossing: 
crossing keeper sets the crossing for WHR train

- Train passes over the Cambrian Crossing

- Crossing keeper resets the Cambrian Crossing for NR trains

- Train passes over the Snowdon Street strike-in treadle: 
Provided this is within 30 seconds of passing over the Cambrian Crossing, then the Snowdon Street crossing warnings will start.

- Train passes over the Snowdon Street automatic crossing

- Train passes over the Britannia Bridge strike-in treadle:
Provided this is within 90 seconds of passing over the Snowdon Street crossing:
	a) Britannia Bridge crossing warnings start
	b) train-approaching annunciator sounds at Harbour Signalbox

- Train passes over the Britannia Bridge crossing

## Loco from Gas Works Siding onto train in Harbour Station

- Loco-crew obtain the token and unlock the ground-frame

- Loco shunted out of the siding

- Loco-crew relock the ground-frame

- Loco proceeds to the Britannia Bridge crossing signal

- Loco-crew telephone Control for permission to enter the occupied platform,
and use the token key-switch to start the Britannia Bridge crossing warnings

- Loco passes over the Britannia Bridge crossing

## Up Works Train arriving Harbour Station from Pont Croesor (out of hours)

- Train passes over the train-approaching treadle: 
annunciator disabled at the Cambrian Crossing when unmanned

- Train stops before the Cambrian Crossing, for the train-crew to operate the crossing

- Train passes over the Cambrian Crossing

- Train stops after the Cambrian Crossing, for the train-crew to reset the crossing for NR trains
(note: the train will pass over the Snowdon Street treadle, but the strike-in will be disabled when the Cambrian Crossing is unmanned)

- Train proceeds to the Snowdon Street crossing signal

- Loco-crew use the token key-switch to start the crossing warnings

- Train passes over the Snowdon Street crossing

- Train passes over the Britannia Bridge treadle, but the strike-in will be disabled when Harbour signalbox is unmanned

- Train stops at the Britannia Bridge crossing signal

- Train-crew use the token key-switch to start the crossing warnings

- Train passes over the Britannia Bridge crossing